## Slide 1: Branch Outbreak Response Team Training
Module 5: Part I
Community Shared Spaces Interventions

## Slide 2
Branch Outbreak Response Team Course structure
Module 1 Overview - Rationale and Role of the Branch Transmission Interruption Team
Module 2
Response triggers and healthcare settings
Module 4 Household risk and interruption (incl. high risk groups)
Module 5 Community shared spaces (incl. high risk groups)
Module 6 Sustaining reduced risk of transmission
Module 3 Understanding cholera transmission
Module 1 Overview - Rationale and Role of the Branch Transmission Interruption Team
Module 2
Response triggers and healthcare settings
Module 4 Household risk and interruption (incl. high risk groups)
Module 5 Community shared spaces (incl. high risk groups)
Module 6 Sustaining reduced risk of transmission
Module 3 Understanding cholera transmission

## Slide 3: Overall purpose
Develop an understanding of risks for disease transmission in community shared spaces, how to intervene in the most effective and efficient way, and how to monitor progress for use in the final evaluation.
Notes: Slides 3-4 Overall purpose and objectives

## Slide 4: Objectives – know how
By the end of the session, participants will understand, for community shared spaces:
Transmission routes of waterborne disease in a community
Food-borne disease and the role of water in further spread in areas with poor hygiene and unprotected stored water.
Effective interventions to break water-borne transmission.
Effective interventions to break food-borne transmission.

## Slide 5: Objectives – show how
By the end of the session, participants will be able to, for community shared spaces:
Undertake household behaviour and risk assessment survey
Practically implement interventions to break water-borne transmission. Mix chlorine solutions and test for residual chlorine
Practically implement interventions to break food-borne transmission.
Community engagement including monitoring.

## Slide 6: Principles of response
EFFICIENCY
  target where risks are common, acting first to stop the sources that affect the most people
GUIDING and CONTROLLING
  if you rely on changing behaviour it will take weeks or months, people will die – give practical support for quick safety improvements.
KEEP IT SIMPLE, MAKE IT CONVENIENT
  Changes you make must be simple (easy to do, not complicated) and convenient (available in the right place) or nobody will apply them
Notes: Slide 6 – Review of principles – which are repeated throughout the training on interventions

## Slide 7: CHOLERA – WATER RISK ASSESSMENT
Notes: Slides 7-16 discuss the ways cholera is transmitted in community areas via water including a group discussion practical on identifying risks.

## Slide 8: Discussion – identifying risks
Groups to discuss among themselves the risks in the following picture (if webinar, then to put their ideas in the chat)
Rank the risks in terms of number of highest to lowest with 1 as highest for greatest risk to greatest number of people. Think about why.
Use the Rapid Risk Assessment C Community shared spaces to help

## Slide 9: Practical – identifying risks
Latrines too close to water sources – river and well
Washing/bathing in river places users at risk of hand / mouth contamination
Surface water use
Well is unprotected – any contact with bucket contaminates bucket and standing water
Open defecation
Water shared between containers for cleaning

## Slide 10: Transmission routes of waterborne disease
The main areas of risk in shared spaces for waterborne disease are:
Drinking water source (contamination from latrine too close, surface water contamination from open defecation bathing), collection (shared containers, contamination from well mouth) and storage (unclean containers, hand contamination)
Bathing water to mouth and nose
Cleaning water to utensils, plates, water containers (unclean water)

## Slide 11: Drinking water
Drinking water, recall, is always going to be the cause of large outbreaks because:
You have to consume a lot of cholera bacilli to get cholera
Cholera bacilli multiple rapidly in water from a few organisms to millions
Everyone drinks water and usually stores it in their homes
There are many opportunities for contamination.

## Slide 12: Drinking water sources
Ground sources may be protected or unprotected wells, springs (piped not equal safe)
Assume all unprotected sources contaminated (no need to test for bacteria as what is clean today will be contaminated tomorrow.)
Protected sources can be bacteriologically testing (once well mouth has been disinfected)
Test residual chlorine - ideally 0.5mg/l after 30 min (0.2- 1.0 mg/l acceptable)

## Slide 13: Drinking water sources
sources are unsafe (cholera occurs naturally and high risk where contact with water)
Source of uncertain risk (trucked, vendor water, food seller water)
Sources of uncertain risk – piped network (depends on treatment and network integrity)

## Slide 14: Drinking water collection
Even water from protected sources (well/spring with pump/apron) is contaminated at collection.
It occurs by contact with the tap/well mouth by hands/containers, both from collector and to collector.
It occurs when collectors immerse hands in bucket
It occurs by sharing water between collectors (rinsing)
A little cholera/bacteria multiplies during storage.

## Slide 15: Water trucking and vendors
What you need to understand:
  Original source of water (where raw water abstracted)
  Stages of transfer down to vendors and households
  Sketch this, identify risk of contamination at each point (same as for household water)
Monitor the drinking water distribution chain and develop control checks to reduce risk of contaminated at each stage

## Slide 16: Food vendors supplying water
Don’t assume that food vendors only supply food. Their water may be contaminated at site or source.
Water, ice and drinks made with untreated water = risk
Source will be similar to households (ground, surface or trucked/piped after ground/surface source, [un]treated?)
There could be common patterns in cholera cases sharing these sources. In 2012, water from vendors was a high risk for cases of cholera

## Slide 17: CHOLERA – FOOD RISK ASSESSMENT
Notes: Slides 17-22 discuss ways cholera is transmitted in community areas by food including a group discussion practical on identifying risks.

## Slide 18: Discussion – identifying risks
Groups to discuss among themselves the risks in the following picture (if webinar, then to put their ideas in the chat)
Rank the risks in terms of number of highest to lowest with 1 as highest for greatest risk to greatest number of people. Think about why.
Use the Rapid Risk Assessment C Community shared spaces to help

## Slide 19: Discussion – identifying risks
Irrigating with dirty water
Cooked food uncovered and cooling
Vendor offering water from open container on ground with scoop
How well is
food cooked?
Handling food with dirty hands

## Slide 20: Transmission routes of food-borne disease
The main areas of risk in shared spaces for foodborne disease are:
Food naturally contaminated.
Food contaminated by hands.
Food contamination from mechanical transfer by flies.
But don’t forget:
Even if food is a cause, water will usually be the main vehicle.

## Slide 21: Food sources
Humans are the main animal reservoir of cholera.
Environmental reservoirs (found in the environment in water) and animal reservoirs (crustaceans and shellfish)
Seafood contaminated before caught, or in storage water
Cholera remains in undercooked food, surviving in crab boiled for up to 8 minutes (2012 Sierra Leone epidemic)
Foods at risk of contamination: rice; millet gruel; vegetables; fruits (not sour); poultry; meat; dairy products
Acidic, dried, salt/sugar-preserved food (salt fish/jam) are safest

## Slide 22: Food contamination - people
Contamination by hands most effective - people clean self after toilet but often don’t wash hands
If a person preparing food in markets and food stalls is ill, or does not show symptoms, spreads quickly
Food becomes contaminated by contact with cutlery or plates washed in contaminated water
Food contaminated by irrigation with infected water (especially close to soil, uncooked, not peeled)
Cholera bacilli on foods rapidly increase in number, left standing at room temperature (must swallow a lot)
Reused, improperly cooked food is a risk

## Slide 23: Food contamination - flies
Though hand contamination is most effective, mechanical transfer by flies is also possible
Usually occurs where food is not refrigerated, and is left uncovered when standing
The type of food, food temperature and ambient temperature determine how rapidly cholera multiply
Refrigeration reduces growth but will not kill it
But remember, hands have a larger surface area and potential for volume of faecal matter than do flies

## Slide 24: Discuss: assessment in special high-risk groups
In your context, what groups might be at higher risk? Think about their shared spaces:
What groups are at higher risk and why?
Will the observations of risk shown here apply to these groups?
Will you have to conduct an parts of assessment differently? Why?
Notes: Slide 23 – discussion on assessment in any special risk groups

## Slide 25
BORT
Branch Outbreak Response Team activity flowchart

## Slide 26
Branch Outbreak Response Team activity flowchart
Rapidly assessing risk
Shared spaces
Module 5 Community shared spaces (incl. high risk groups)

## Slide 27: Practical: RAPID ASSESSMENT
Training Module 5

## Slide 28: Practical assessment
Observe the training site cards placed around the space. Use the rapid assessment tool and ask questions of the community to determine -
1 RISKS (which of the cards represent the greatest risk and why)
2 FURTHER ASSESSMENT (WHAT AND WHERE):
Testing residual chlorine indicator test
Rapid test for faecal coliforms
3 INTERVENTIONS (WHAT WHERE):
Refilling and installing chlorinators (chlorine technical session later)
Bulk water chlorination for trucked water
Handwashing units
Decommissioning latrine(s)
4 COMMUNICATION, MONITORING, SUSTAINED RESPONSE:
Signs and instructions (including for food venues)
What oversight and monitoring needs to be in place from beginning?
Sustainable fixes for chlorine, handwashing water and soap
Notes: Slides 27 This practical is designed to encourage participants to identify risks in a rapid needs assessment of community spaces.
Main points after the exercise are:
Water is always going to be a main consideration, even if food is involved (unless there is chlorinated, piped water with a reliable unbroken network)
Focus should be on water treatment even before a source is identified (though samples can be taken and recorded in advance of treatment)
Food is important, but questions should reveal that this risk is low
Handwashing in the absence of 1-2 is largely pointless. Clean hands and dirty water = cholera.
In the end participants should have identified risky water sources, and recommended testing and treated water immediately, installed handwashing units at water collection points and food vendor areas with signs. They should also have enquired about the source of the water for the internet shop. Other appropriate interventions they consider are useful.

## Slide 29: CHOLERA WATER INTERVENTIONS
Notes: Slides 27-39 cover action to break cholera transmission in community areas. Some videos are embedded.
The main focus is chlorination at source, which will be effective even without handwashing, home water treatment, changing water containers, etc.
Handwashing units are also covered.
Chlorination can be passive (best) or active (where we rely on the user dosing the water).
Reminder not to forget food vendors as they serve water, and can be responsible for outbreaks, and water which is imported/trucked.
Decommissioning latrines close to water points or open water is also included.

## Slide 30: Drinking water interventions
You cannot develop water, sanitation and hygiene infrastructure because you have:
  Insufficient staff/volunteers
  Insufficient materials and funds
  Insufficient time (there is an outbreak so an emergency)
TEST: 1) chlorine level (assume all may become contaminated); and 2) bacterial level (protected sources)
Be EFFICIENT – target where risks are common, acting first to stop the sources that affect the most people
GUIDE and CONTROL – if you rely on changing behaviour it will take weeks or months, people will die
Changes must be SIMPLE (not complicated), CONVENIENT (available in the right place) or nobody will apply them

## Slide 31: Treating at source
Treating at source will always be the most efficient, but it may not be where contamination occurs
Chlorinate to ensure residual levels at household, helps if contamination occurs further along the chain
Treating at source is easiest with protected groundwater (passive chlorinators)
Treating at source is more difficult with surface water: active chlorinators (mean choice and people may not do it); or bucket chlorination (requires permanent staff stationed, estimate container doses)

## Slide 32: Active/passive chlorination at pump

## Slide 33: Active chlorination at surface collection
What could go wrong?
People don’t use it
People use it incorrectly
But there are things you can do

## Slide 34: Ensuring active chlorinators are used
In practice, people will not use an active dispenser (0-28% use) without the following being in place:
source selection (sited in the right place)
chlorine solution quality and supply chain
hardware maintenance
promoter remuneration
experienced program staff (RC has this)
working with local partners (RC is this)
regular monitoring
integration into larger WASH programming, and
establishing a sustainability plan
With these, 63-81% effective use

## Slide 35: Passive chlorination at pump collection
There is little for the user to do. There is no measurement/ dosing, just filling containers as normal. Only replenishment of chlorine is required by someone in the community

## Slide 36: Signs
PLEASE READ
1 Wash your hands
2 Add a little of the treated water
3 Shake thoroughly to clean, and empty.
DO NOT SHARE water with other people's containers.
4 Fill your container with the treated water.
5 WAIT 30 MINUTES BEFORE DRINKING. This water is treated with chlorine and it will take time to kill any bacteria in the water.

## Slide 37: Signs

## Slide 38: Introduction to hardware
JENGU
https://jengu.org.uk/jengu-assembly-instructions-video/

## Slide 39: Introduction to hardware
EVIDENCE ACTION Active chlorinator https://www.youtube.com/watch?v=QcdH3QbHyuE
Other active and passive chlorinators are available

## Slide 40: Introduction to hardware
Zimba (8 min 40 sec) – already in production
https://youtu.be/KSxkZKdmhj4v=QcdH3QbHyuE
Other passive chlorinators may be available

## Slide 41: Action in trucked and vended water
Trucked water we can assume is not chlorinated (as chlorine accelerates corrosion so truck supplier discourage its use)
Sketch the supply chain to identify contamination risks and places where interventions can be initiated
1 confirmation – take sample for testing of residual chlorine level. Optional - presence of faecal coliform – negative does not mean safe.
2 removal of risk (sources of excrement, container contamination – as for other sources, act if possible)
3 Bulk chlorinate before distribution (close to source)

## Slide 42: Trucked/vended water treatment
For most complete coverage, with the least effort, treat the water as close to source as the situation allows after testing for chlorine level*
*The most common test is the dpd - diethyl paraphenylene diamine - indicator test, using a comparator. This test is the quickest and simplest method for testing chlorine residual.

## Slide 43: Training for those in the chain
Training vendors / trucking operators on drinking water chlorination, provide them with access to chlorine.

## Slide 44: Food vendor water treatment
Ensure that food vendors’ stored water is protected and disinfected. This is important as it is a common source for many people (the reason it was a common source in the 2012 epidemic of cholera in West Africa)
Training for water vendors on proper drinking water disinfection could be combined with water trucking operators
Provide them with access to chlorine for future use.

## Slide 45: Removal of bulk contamination risk - decommissioning a latrine
A HANDOUT on how to decommission a latrine is supplied with these slides
Notes: Add a link to the latrine decomissiong. Here it would be good to add the step by step guide to decomission latrines.
Here the link http://josephashmore.org/publications/latrines-decommission-Pakistan.pdf

## Slide 46: CHOLERA FOOD INTERVENTIONS
Notes: Slides 40-42 cover action to reduce foodborne cholera.
Principles are: Sterilized, Hot, Covered, Hands (SHoCH). Water containing uncooked seafood should be sterilized, crabs and other shellfish should be boiled for 15 minutes. Serve hot, keep covered against flies, wash hands.

## Slide 47: Food interventions
You probably cannot intervene in every private businesses behaviour because you:
  Are not a regulatory agency
  Have insufficient time (there is an outbreak so an emergency)
Be EFFICIENT – target where risks are common, influencing those higher risk vendors that affect the most people
GUIDE and CONTROL – if you rely on changing behaviour it will take weeks or months, people will die – give practical support for quick safety improvements. Don’t forget water!
Changes you make must be SIMPLE (easy to do, not complicated) and CONVENIENT

## Slide 48: Food health protection
Encourage vendors to ensure their products are: SHoCH
STERILIZED: Seafood like crabs boiled for 15-20 minutes, no raw shellfish. Sterilizing water they are in with chlorine. Also, drinking water.
HOT: Well cooked, served hot.
COVERED: Food to be covered to protect from flies (cover makes contact with flat suface, no gaps.
HANDS: practical assistance for vendors and users (hand washing enabling technology, soap and water or alcohol hand gel).
It’s pointless to simply tell people to wash their hands – nothing will change! Remember, make it convenient!

## Slide 49: Review of principles
EFFICIENCY
  target where risks are common, influencing those higher risk vendors that affect the most people
GUIDING and CONTROLLING
  if you rely on changing behaviour it will take weeks or months, people will die – give practical support for quick safety improvements.
KEEP IT SIMPLE, MAKE IT CONVENIENT
  Changes you make must be simple (easy to do, not complicated) and convenient

## Slide 50: Discuss: actions in special high-risk groups
In your context, consider the high risk groups you have identified. Ask:
Of those solutions presented for water and food, what will work? (action to be taken to interrupt transmission)
Of those solutions presented for water and food, what will have to be done differently for these high risk groups?
Remember that you might not have the materials, staff, transport, etc., to respond effectively to all groups so try to be realistic.

## Slide 51: BREAK
Eat safe!
Set up the room for the practical
Notes: Use this time to set up the room with cards for the practical.

## Slide 52
BORT
Branch Outbreak Response Team activity flowchart

## Slide 53
Branch Outbreak Response Team activity flowchart
Interrupting transmission
Shared spaces
Module 5 Community shared spaces (incl. high risk groups)

## Slide 54: Practical: INTERRUPTION
Training Module 5

## Slide 55: Practical Interruption
Observe the training site cards placed around the space. Use the rapid assessment tool and ask questions of the community to determine -
1 RISKS (which of the cards represent the greatest risk and why)
2 FURTHER ASSESSMENT (WHAT AND WHERE):
Testing residual chlorine indicator test
Rapid test for faecal coliforms
3 INTERVENTIONS (WHAT WHERE):
Refilling and installing chlorinators (chlorine technical session later)
Bulk water chlorination for trucked water
Handwashing units
Decommissioning latrine(s)
4 COMMUNICATION, MONITORING, SUSTAINED RESPONSE:
Signs and instructions (including for food venues)
What oversight and monitoring needs to be in place from beginning?
Sustainable fixes for chlorine, handwashing water and soap
Notes: Slides 49-50 This practical is designed to encourage participants to identify risks in a rapid needs assessment of community spaces.
Main points after the exercise are:
Water is always going to be a main consideration, even if food is involved (unless there is chlorinated, piped water with a reliable unbroken network)
Focus should be on water treatment even before a source is identified (though samples can be taken and recorded in advance of treatment)
Food is important, but questions should reveal that this risk is low
Handwashing in the absence of 1-2 is largely pointless. Clean hands and dirty water = cholera.
In the end participants should have identified risky water sources, and recommended testing and treated water immediately, installed handwashing units at water collection points and food vendor areas with signs. They should also have enquired about the source of the water for the internet shop. Other appropriate interventions they consider are useful.

## Slide 56: Constructing Jengu
JENGU
https://jengu.org.uk/jengu-assembly-instructions-video/
Notes: Slide 48 After or during a break a video on assembling a rapid response handwashing unit which can be connected to any container.

## Slide 57: Practical – Handwashing
Handwashing with soap and water (where to site in area near training site):
Needs assessment based on other interventions, engaging communities on training site – where are hygiene risks?
Installing hands-free handwashing technology – where to site
Securing hygiene materials (solid soap, liquid option) – how will you do this? Discuss
Efficient regular water supply – what are the options. Remember, the more frequently refill needed, more chance it will be empty
Additional considerations:
Signs and instructions
Initial oversight and monitoring
Drainage

## Slide 58: Review of principles
EFFICIENCY
  target where risks are common, influencing those higher risk vendors that affect the most people
GUIDING and CONTROLLING
  if you rely on changing behaviour it will take weeks or months, people will die – give practical support for quick safety improvements.
KEEP IT SIMPLE, MAKE IT CONVENIENT
  Changes you make must be simple (easy to do, not complicated) and convenient
Notes: Slide 52 – Review of principles, repeated throughout the training on interventions.

## Slide 59: Community Engagement and Monitoring
Throughout the process, ensure community members know what you are doing, and why. They will support activities.
We have included a simple form to manually collect information on chlorination and handwashing at water collection.
Notes: Slide 53 is a short exercise about COVID-19 risk which can be done in the area of the training.

## Slide 60: Key messages
Water will always be a risk for cholera even if food is implicated
Identify water risks but assume all water is contaminated OR has potential for contamination
Take test samples if available, treat water using passive or active methods and show signs
Vendor risks - education, handwashing facilities, don’t forget food vendors’ water!

## Slide 61
Module 5 – Part II Chlorine solution materials, applications and preparation

## Slide 62: Training Module Agenda
Material handling / Health and Safety / Storage
Products / materials for Chlorine solution production
Devices to produce chlorine from saline
Mixing solutions for water disinfection
Solution Preparation, Concentrations, Testing (Free Residual Cl, NTU and pH)
Practical: Use of GTFCC App
Notes: Slide 55 – agenda for second half of community training.
Refer to R1 comments

## Slide 63: Material handling, health & safety
Product is dangerous – it is bleach!
Prepare in well ventilated areas using wood spoon/stick to mix (no metal).
Prepare solutions daily. Don’t create large quantities.
Don’t mix NADCC and HTH
Don’t combine disinfectants, can cause respiratory irritation and release potentially fatal gases (particularly combined with hypochlorite solutions)
Use and label containers (do not put in drinking containers) Label as “not for drinking /bathing” XX% Chlorine Solution for YY purpose (depending on the concentration and intended application)
Notes: This means that if you see some cases, there might be more.

## Slide 64: Material handling, health & safety PPE
Keep solution in dry, shaded place, not exposed to heat, sunlight (burns off chlorine), out of reach for children !
Recommended PPE are:
  rubber gloves
  thick apron
  closed toe shoes
  face mask / respirator and eye protection such as safety glasses to avoid splashes
Notes: Slide 70 – Health and safety – very important to reduce eye damage, burns, inhalation.
This means that if you see some cases, there might be more.

## Slide 65: Materials for disinfection
Products and methods for water disinfection differ between places. They may also differ between response types (emergency, development, health facilities, schools)
Use of Kit 001 - https://itemscatalogue.redcross.int/emergency-preparedness
Products/solutions recognised by the IFRC / RCRC include:
HTH Calcium Hypochlorite - Ca(ClO)2 (60 – 70% Active Chlorine]
Aquatab pills - NaDCC – (60% Active Chlorine – One tablet containing 1.67g NaDCC releases 1g available chlorine when it is dissolved in water)
Household Bleach - NaClO 4 - 6% active Chlorine
Wata – production of chlorine by electrolysis
Notes: Slide 56 – overview of types of materials for water disinfection.

## Slide 66: Making Chlorine 1: WATA Unit
WATA Standard Unit Chlorine Production
Production time: 2 hours
Production volume: 2L sodium hypochlorite at 5g/L
Quantity of chlorine produced: 10 g of active chlorine
Dimensions of device: 15 x 6 x 5 cm
Kit contents
One WATA-Standard device + control box +15V/5A power supply
One 50 mL syringe
One production bottle
One WataTest kit
One WataBlue kit
User Manual
pH Test Kit
Solar Kit (optional)
Notes: Slides 57-58 Introduction to the Wata device including concentrations of solution for different purposes (Wata is covered in a separate module).

## Slide 67: Making chlorine 2: MSR Chlorine Maker
MSR Chlorine Maker (NaCl + H2O + ENERGY → NaOCl + H2)
Production time: 7 min
Production volume: 50ml sodium hypochlorite at 8g/L (50ml of 0.8% Cl) – sufficient for 200L (or 10 jerry cans)
Dimensions of device: 25 x 11 x 5cm
Kit contents
User Manual on box
pH Testing strips
Additional
Battery
Mains adapter (optional)
Solar Kit (optional)
Notes: Slides 57-58 Introduction to the Wata device including concentrations of solution for different purposes (Wata is covered in a separate module).

## Slide 68: MSR Chlorine Maker
https://youtu.be/Dwsx4EpKkKg
Notes: Slides 57-58 Introduction to the Wata device including concentrations of solution for different purposes (Wata is covered in a separate module).

## Slide 69: Solutions for disinfection (Wata)
Different treatments required based on need
Wata product is 0.5% chlorine (i.e. 5 g/L)
0.5% solution for heavily contaminated surfaces - widespread faeces, vomit (treatment centre) – no skin contact it burns
0.05% solution for handwashing (1 litre of Wata stock solution mixed with 9L water 1+9=10 or, 0.5% diluted 10x)
Drinking - every 10 litres add 6ml* (syringe) = 3ppm or 3mg/L
% of active chlorine in the solution | Main purpose
0.50% | Wata Stock Solution (2 litres)
0.50% | blood and body fluids large spills
0.20% | Surfaces and item disinfection
0.05% | Hand and dishwashing
*approximate – depending on residual chlorine jar tests

## Slide 70: Chlorine solution according to use
SURFACE DISINFECTION WITH DIFFERENT PRODUCTS |  |  | 
 | 0.05% | 0.2% | 2%
HTH (70% active chlorine | 1 table spoon in 20 litres of water | 1 table spoon in 5 litres of water | 2 table spoons in 1 litre of water
Bleach (5%) | 14 table spoons in 20 litres of water or ¼ cup in 20 litres of water | 20 table spoons in 5 litres of water | 2 cups in one litre
Use | Washing hands and clothing (soak for 15 minutes) Skin disinfection | Disinfecting of beds, floors, latrines, kitchen, utilities of patient, etc | Disinfection of vomit and stool. Disinfecting dead bodies (clean or spray with this solution before last offices)
Precautions | Solution must be changed every day and protected from heat and light | Use with gloves Solution must be changed every day and protected from heat and light | Use with gloves Solution must be changed every two days and protected from heat and light
Notes: Slide 59 – chlorine solutions for Surface treatment and guiding caution.

## Slide 71: Water disinfection with different products
Producing a standard 1.0% solution of differing water concentrations will differ between products
Notes: Slides 60-63 Treating water and ensuring residual chlorine levels. This is important as it allows deactivation of pathogens if contamination occurs later (dirty hands, utensils, scoops, container).

## Slide 72: Factors affecting effectiveness
Residual chlorine depends on variables in the water:
  Suspended solids, described as turbidity or nephelometric turbidity units (NTU)
  pH, acidity - alkalinity
< 5 NTU should be the aim; above 5 NTU, higher chlorine doses or contact times required to inactivate microorganisms. Above 5 NTU requires flocculation and filtration
pH ideally 6-8. Above pH 8.0, higher chlorine and/or contact times required to inactivate microorganisms. Below 6.0, treatment will be compromised
Residual Chlorine should be 0.5 mg/L Bench/jar test using a pool kit testing reagent (“pool” test, by litmus paper or similar reagent)

## Slide 73: Testing residual chlorine in water

## Slide 74: Testing residual chlorine in water
Jar Test Method: Produce 1L of a 0.5% stock solution using the available Chlorine (guidance – look at the GTFCC App)
Add volumes of 0.5% solution (from Wata device) in the following quantities to buckets or jerry cans of known volumes (10L is good) with syringe, as indicated in table.
The container with residual close to 0.5mg /L - use that dose (e.g. 5ml per 10L)
Give main treatment team member with electronic chlorine meter (can also use pool testing kits or chlorine disc)
Bucket 1 | 2ml
Bucket 2 | 3ml
Bucket 3 | 4ml
Bucket 4 | 5ml
Bucket 5 | 6ml
Bucket 6 | 7ml

## Slide 75: Exercise – Use of GTFCC App
Q - Calculate out the necessary quantity of HTH product (70% free chlorine) required to produce 10L of 2% Chlorine Solution?
A –
Q – What concentration of solution is produced with is required to produced 10 mL of Bleach and 1 L of water?
A –
Notes: This means that if you see some cases, there might be more.

## Slide 76: Answer – Use of GTFCC App
Q - Calculate out the necessary quantity of HTH product (70% free chlorine) required to produce 10L of 2% Chlorine Solution?
A – 300 grams
Q – What concentration of solution is produced with is required to produced 10 mL of Bleach and 1 L of water?
A – 0.05 %
Notes: This means that if you see some cases, there might be more.

## Slide 77: Exercise – Use of GTFCC App
Q - Calculate the necessary quantity of HTH product (70% free chlorine) required to produce 1L of 1% Chlorine Solution for drinking water stock solution?
A –
Q – What are the ideal parameters for water quality (ntu, pH) to provide for effective disinfection? What is the ideal residual chlorine content (for a 24 hours period)
A –
Notes: This means that if you see some cases, there might be more.

## Slide 78: Answer – Use of GTFCC App
Q - Calculate the necessary quantity of HTH product (70% free chlorine) required to produce 1L of 1% Chlorine Solution for drinking water stock solution?
A – 15 grams
Q – What are the ideal parameters for water quality (ntu, pH) to provide for effective disinfection? What is the ideal residual chlorine content (for a 24 hours period)
A – ntu < 5, 6.0 <pH <8.0, 0.5mg/L
Notes: Slides 65-68 Practicals on calculating chlorine dosing.
This means that if you see some cases, there might be more.

## Slide 79: Scenario - Household
You are presented with a household a member who has become ill with cholera. You are required to provide a description of how to purify household water for consumption, and create a standard stock solution for handwashing.
Q. What concentration is required for handwashing and water purification solution? What is the amount of HTH required to produce 1 L of this solution?
Notes: Slides 71-72 – Practical exercises on household and facility chlorine calculations.
This means that if you see some cases, there might be more.

## Slide 80: Key messages
Prepare safely with right equipment
Ensure right concentrations of chlorine for the type of use and test it
Use the GTFCC app to assist you
Don’t make more chlorine than you need (remember, it is prepared or synthesised quickly, but does not store well)
Keep out of reach of children and store in a clearly marked container (that is not recognisable as a drinking bottle!)