## Slide 1
Date, Place
Module 4:
Household interventions
Branch Outbreak Response Team Training
Notes: Register participants
Official opening and recitals

## Slide 2
Branch Outbreak Response Team Course structure
Module 1 Overview - Rationale and Role of the Branch Transmission Interruption Team
Module 2
Response triggers and healthcare settings
Module 4 Household risk and interruption (incl. high risk groups)
Module 5 Community shared spaces (incl. high risk groups)
Module 6 Sustaining reduced risk of transmission
Module 3 Understanding cholera transmission
Module 1 Overview - Rationale and Role of the Branch Transmission Interruption Team
Module 2
Response triggers and healthcare settings
Module 4 Household risk and interruption (incl. high risk groups)
Module 5 Community shared spaces (incl. high risk groups)
Module 6 Sustaining reduced risk of transmission
Module 3 Understanding cholera transmission
Notes: On the final point: the idea is that any emergency response should lift the community to a higher point capacity and prevention wise than before the outbreak. Emergency operations tend to create a lot of data on the target areas and also involve training, awareness raising and access to equipment. All of these things should be used in a way that has one eye on actions that might be taken after the outbreak and which might help prevent its reoccurrence..

## Slide 3: Overall Purpose
For participants to know how to:-
Identify case households and clusters of at-risk of contamination and risk practices households.
Transmission routes in Cholera at Household level.
Interventions BORT can undertake in the household while linking with community interventions to ensure there is no duplication.​​
Notes: Slides 2-5 Overall purpose, objectives, agenda
which can be undertaken in the home and the contents of a household kit. Finally, it will consider how to coordinate household and community actions to ensure there is no duplication.
Tier 2 moves the focus away from health facilities and to those households where cases have been confirmed. In coordination with the District Health Authority (DHA), permanent health facilities and temporary ones such as CTCs, CTUs and ORPs, the BORT identify clusters of case households where transmission breaking interventions can be carried out.
This module gives the rationale for prioritizing case households and identifies key areas of transmission. It then considers interventions which can be undertaken in the home and the contents of a household kit. Finally, it will consider how to coordinate household and community actions to ensure there is no duplication.

## Slide 4: Objectives – know how
By the end of the session, participants will understand the following regarding case households:
Transmission of faecal routes and waterborne disease in a household
Food-borne disease and the role of water and faecal matter in further spread in households with poor hygiene and unprotected stored water.
Effective interventions (key protective behaviours) to break faecal and water-borne transmission routes at HH level.
Effective interventions to break food-borne transmission at HH level
Content of the Household Hygiene and disinfection kit

## Slide 5: Objectives – show how
By the end of the session, participants will be able to carry out the following in case households:
Practically implement interventions (key protective behaviours) to break the faecal routes and water-borne transmission routes using the Household Hygiene and Disinfection kit (HHD).
Practically implement key protective behaviours interventions to break food-borne transmission using the HHD.
Community engagement implement including monitoring.

## Slide 6: Training Module 4 Agenda
The rationale behind household interventions (key protective behaviours)
How to work with DHA to identify the households where interventions will take place
What interventions will be carried out and how they will be implemented
What the contents of the HH Hygiene and Disinfection Kit are for and what the key messages are for affected households.
Practical Session on the Household Rapid Sanitary observations checklist and actions using the kits

## Slide 7: Principles of response
EFFICIENCY
  target where risks are common, acting first to stop the sources that affect the most people
GUIDING and CONTROLLING
  if you rely on complex changing behaviour it will take weeks or months, people will die – give practical support for quick, simple safety improvements.
KEEP IT SIMPLE, MAKE IT CONVENIENT
  Changes you make must be simple (easy to do, not complicated) and convenient (available in the right place) or nobody will apply them
Notes: Slide 6 Principles of response – These messages is repeated throughout the modules on practical action

## Slide 8: Cholera Risk: Proximity
Whilst several factors should be included in assessing risk, studies suggest that proximity to the cholera case is a key indicator.
Same Household 100x greater risk
Less than 50 metres 36x greater risk
Less than 100 metres 6x greater risk
Less than 150 metres 5x greater risk
Notes: Slide 7-8 – Rationale for case household and neighbor interventions - high risk because of shared resources (e.g. water extraction equipment)

## Slide 9: Why Household level interventions Cholera
80% cholera transmission is within the household (intra household transmission).
Household contacts have 100 times risk of cholera
V. cholerae is hyper-infective during first 7-10 days of shedding from cases, thus interventions in case households should be carried out immediately.
Transmission through shared drinking water, shared toilets, contaminated food and caring responsibilities is more likely within a household

## Slide 10: Targeting and Visiting Households
In an outbreak there needs to be careful targeting in order to use the limited resources to the best effect.
‘Blanket’ distribution of kits to households should be avoided.
Initial targeting will be case households indicated from the line lists* of health facilities and coordinated with District Health Authorities.
Household level interventions should take place as soon as possible.
If possible, contact household and village authorities before visit to explain the purpose. Move to the village with enough kits for the case household(s) and a small buffer stock
Notes: *Line list: table containing information about cases in an outbreak; each row represents a case and columns represent variables such as demographic, clinical and epidemiologic information (e.g. risk factors and exposures).
Slide 9-12 – the process of visiting households including timing, protocol and sensitivity
Ask the audience , if there are taboos on cholera and Chlorine, during responses or intervention in cholera intervention.

## Slide 11: Targeting and Visiting Households
The approach to a household should be done with a village leader and be kept low-key. It is important to avoid any sort of panic in the community or stigmatization of the case household.
Introduce the team, explain the reason for visiting and the planned actions.
It is important that, if possible, actions at both HH and community level are happening concurrently. Some actions in the community shared spaces will be based on the answers to questions asked at household level.
Notes: Heard there were notes on minimum package for CEA in emergencies from Sharon. Not that there is something spectacular but you could have a look for inspiration. Especially on the engagement part.

## Slide 12: Visiting Households: Sensitivity
Avoid identifying the case household publicly, which can result in shame or shunning of its members. If a single HH is visited its members may experience stigma or be ostracized by the community.
Individual volunteers visiting households may be viewed negatively, especially in cases such as single women led households. Visiting with a village leader and going in pairs can help avoid rumors and suspicion.
It is recommended that two volunteers work together going from household to household and that a group of HHs rather than a single one are targeted.
Notes: Heard there were notes on minimum package for CEA in emergencies from Sharon. Not that there is something spectacular but you could have a look for inspiration. Especially on the engagement part.

## Slide 13: Visiting Households: Sensitivity
Question:
How likely is stigmatization from cholera in your community?
Please discuss as a group and produce strategies to overcome this.
Notes: Facilitate and ask participants, prompt and ask for example in their context

## Slide 14: Visiting Households: investigations
Introduce the reason for the visit and describe what actions will be taken.
Observe and ask questions about the cholera patient: their routines, facilities in the household and in the community they use. Is there any other family member or neighbor with the same symptoms.
One team member goes with the community leader to the community facilities described.
Based on observations and answers to questions carry out relevant actions in the household.

## Slide 15: Visiting Households: Immediate actions
Before any investigation/observation, we assume all stored water is at risk of contamination
All stored water must be chlorinated in house and neighbouring houses
Any system of water use which involves submerging a container like a cup or scoop should be replaced with a covered container with a tap. Repeat for neighbours if supplies permit.
Any food which the case had prepared or had contact with should be put into the waste and steps taken to ensure no flies can come into contact with it.
Notes: Immediate action, investigation (in that order)
Heard there were notes on minimum package for CEA in emergencies from Sharon. Note that there is something spectacular, but you could have a look for inspiration. Especially on the engagement part.

## Slide 16: Visiting Households: feedback
Think about potential unintended consequences of the activities you are planning. Could these affect their safety or dignity, increase discrimination or limit access to services and information?
Ensure a system is in place to take and answer questions and complaints. Share important information clearly, honestly and in a way the community can understand - e.g. when services will stop, what will happen next, what role for the community, how to get in touch with the NS
Tackle rumours quickly by addressing them and providing the correct information.
Notes: Communication and investigation observation with households

## Slide 17: ACTIVITY 1
Think about the usual transmission routes of Cholera covered in module 2, using the handout provided:-
Make a list of observations and 'show me' requests you will ask the members of the household.
Put these in 4 categories: 1) Safe water, 2) Safe sanitation and handwashing 3) Food 4) Cleaning / hygiene practices
Circle 'community link' questions*
You have 30 minutes
(15 mins group discussion/ 15 mins presentation)
Notes: *Community link observations are ones which link the household into the community. For instance, observation of the water storage vessel in the home is a household observation/question, whereas where do you collect your water from will probably be a community link question as it ties the household to the community.
Community link observations updated with the observation list
Where do you collect water from and what container do you use to collect the water?
Did the case eat food that was prepared or stored outside the home?
Do people from outside the household share the toilet facilities you use?

## Slide 18: Cholera Transmission Risks in the Case Household
Common drinking water storage, treatment and serving techniques.
Common preparation and handling of food
Care responsibility contact and proximity
Common sanitation and hygiene locations
Common area of habitation which will be cleaned by certain members of the family.
Clothes and other linen cleaned together
Notes: Cholera transmission risks and preventions: we follow the 5 section of the household checklist

## Slide 19: Activity 2 Get familiar with the Household Rapid Sanitary observations checklist, the actions and the kit (scenarios)
Look at the checklist – household direct observations:
Safe water use;
Safe sanitation and handwashing habits;
Food hygiene habits
Cleaning / hygiene practices
Notes: We focus on each of the five component at a time
Please look at the survey below, discuss in your groups what actions you are going to undertake? You need to decide whether you give them a kit or not and the specific actions needed to be undertaken by the volunteers for the areas related to water use for drinking? (you have 5 minutes)

## Slide 20: 2 Get familiar with the Household Rapid Sanitary observations checklist, the actions and the kit
Discuss the “notes for Volunteers” column in the observations check list for each of the 5 sections
Go through the observations one by one, discuss in your group and then see the corresponding actions.
The kit contents is used to encourage the key protective behaviours.
Notes: Practical activity on the Household Rapid Sanitary observations checklist and actions (key protective behaviors)
Mod4 Rapid Risk Assessment Tools BORT document
Present the list the observations and ask the participant to list the related actions (key protective behaviors) for each observation - Key protective behaviors to stop the cholera transmission route. (Refer to the F diagram). Hide the column with the actions (Key protective behaviors). Then the facilitator complement with the actions that were not mentioned by the participants.

## Slide 21: Key Actions to Reduce Cholera Transmission Risk in the Case Household
Treatment of drinking water ensuring residual chlorine. Safe drinking water storage and serving techniques preferably from a bucket with tap.
Ensure safe and disinfected common sanitation and hygiene locations
Practice of personal hygiene (i.e., handwashing, body hygiene)
Practice food hygiene during the preparation and handling of food and its safe storage.
Practicing personal hygiene before, during and after care responsibility contact and proximity to case. No sharing of plate, other materials, between case and household members
Notes: Key actions to reduce transmission: water; food; safe caring for cases; cleaning of common hygiene/sanitation facilities
Link with the observation and practical actions of the HH Sanitary Survey.
In the following slide we are going in the details of the actions and the corresponding Kit component for each of the 5 components.
Key actions to reduce transmission in priority of risk: water; food; disinfection of the case area; cleaning of common hygiene/sanitation facilities
Link with the observation and practical actions of the HH Sanitary Survey.
In the following slide we are going in the details of the actions and the corresponding Kit component for each of the 5 components.
Note that the visit begins and ends with the duty of care to the ill.

## Slide 22: Priority actions to interrupt cholera transmission in case household
Case: Ensure cases access medical care if cannot hydrate.
Water: All water is contaminated. Immediately chlorinate all stored water, ensure residual chlorine. Store water in container with tap, no dipping utensils. Ensure clean ORS for all cases.
Disinfection area: Install point for handwashing and material disinfection (water+Cl), near case/kitchen, for team/household – use after contact contaminated materials
Food: If possible sterilize contaminated foods, else destroy. Disinfect food preparation materials, ensure safe storage.
Case area: Disinfect areas contaminated by cases including anything they used for vomit/shit (e.g. bucket), remove + disinfect soiled clothes (see 3), linen, other items
Latrine: Ensure safe and disinfected sanitation area with handwashing facility including soap (someone very ill is unlikely to be able to use a latrine but mild cases might)
Handwashing
Note that there handwashing section is integrated with sanitation and hygiene. Handwashing is required in all of the actions by the team (and household members). Gloves are for protection against chlorine only. Gloved and ungloved hands should be washed as normal unless gloves are disposed of between actions. Water disinfection cannot wait for a household tippy tap to be constructed. Team should use communal handwashing (Jengu).
Notes: Doble slide: Key actions to reduce transmission in priority of risk: water; food; disinfection of the case area; cleaning of common hygiene/sanitation facilities
Link with the observation and practical actions of the HH Sanitary Survey.
In the following slides we are going in the details of the actions and the corresponding Kit component for each of the 5 components.
Note that the visit begins and ends with the duty of care to the ill.
Key actions to reduce transmission in priority of risk: water; food; disinfection of the case area; cleaning of common hygiene/sanitation facilities

## Slide 23: 1. Cholera case in the household
Connect household to ORP or community ORS volunteers
Give access to clean water for making ORS
Ensure cases access medical care if cannot hydrate
Note that your visit begins an ends with a duty of care to those with cholera disease.
Notes: If you have a case in the household is about priority action related to health care. When they go to neighbour house, and someone got cholera. This is showing the priority they should take, health priority of the case.
Check with the actions in the household observation checklist

## Slide 24: 1. Cholera case in the household - resources
ORS should be held by volunteers or ORP teams
Kit for water disinfection
Household cloths and 0.2% Cl solution to clean containers
Team transport if needed
Notes: Check with the actions in the household observation checklist

## Slide 25
Actions, Training and Guidance to give household
Set up bucket with tap (non-contact device) (and demonstrate)
Demonstrate filtering water using a cloth (if turbid)
Treat existing HH water if not already treated, demonstrating use of water disinfection products (refer to module 5)
Tape the info card to the wall where water is stored
2. Water Treatment, Storage and Serving
Notes: Check with the actions in the household observation checklist

## Slide 26: 2. Water Treatment, Storage and Serving
What the Kit contains to achieve this:
10 litre bucket with tap
Water treatment products for 4 weeks
Cloth for filtering water with thick elastic band
Information card on the use of the water treatment sachets
Tape

## Slide 27: 3. Disinfection area
Install disinfection place for textiles (0.2%Cl)
Install handwashing facility
Notes: Check with the actions in the household observation checklist

## Slide 28: 3. Disinfection area - kit
What the Kit contains to achieve this:
Soap (for handwashing and body)
Jerry can, string, wood for tippy tap
10 litre bucket, cloths and disinfectant (chlorine)
Laundry soap
Info card: handwashing frequency.
Info card: parts of hand often missed.
Notes: Check with the actions in the household observation checklist

## Slide 29: 4. Food handling, preparation, storage
Actions, Training and Guidance to give household
Ask household members to describe preparing meals.
Particular attention should be given to seafood and fish if these are consumed in the household
Treat water to be used for food preparation
Discuss food storage options and demonstrate the use and the purpose of the food cover.
Ask about hand washing at meal-times
Explain that cases should not share plates, other materials, with other household members
Surface disinfection (concentration of 0.2% chlorine for surface disinfection)
Notes: Check with the actions in the household observation checklist

## Slide 30: 4. Food handling, prep, storage - kit
What the Kit contains to achieve this:
Soap handwashing and dishwashing
Info card: food preparation
Info card: handwashing frequency.
Info card: parts of hand often missed.

## Slide 31: 5. Disinfection of case area
Install material disinfection place (0.2%Cl) + handwashing
Disinfect areas where case is/was (and demonstrate)
Cleaning surfaces thoroughly and remove soiled items
Cleaning cloths, soiled clothes, linen (+demonstrate)
Soak in chlorine 0.2% solution 10 min, rinse soap water
Soiled water should be disposed of in the latrine pit
Hung to dry in the sun
Remember that any water which has not been sterilised will be a potential source of onward contamination.
Body fluids:
Give patient bucket solely for vomit /faeces (no other use)
Add 2% bleach/chlorine (MSF), regularly dispose in latrine
Notes: Check with the actions in the household observation checklist

## Slide 32: 5. Disinfection of case area - kit
What the Kit contains to achieve this
(already covered in 3)
Notes: Check with the actions in the household observation checklist

## Slide 33: 6. Sanitation and hygiene facilities
Actions, Training and Guidance to give household
If practice open defecation advise to bury the faeces, not near any body of water, similarly children's faeces.
Establish convenient handwashing. Demonstrate effective handwashing using diagram of parts of hand often missed
Demonstrate methods for economical use of soap such as dissolving shavings in water
Demonstrate disinfecting and clean latrine.* Ensure water stationed for cleaning and flushing. (concentration of 0,2% chlorine for surface disinfection)
Latrine hole should be covered where possible (and use sticky fly paper to catch flies)
Ensure hand wash facility with soap and water beside the latrine by constructing tippy tap if necessary, with drainage
Notes: Check with the actions in the household observation checklist
* often the floor of latrines will be mud and difficult to clean properly. Situating plastic sheeting around the toilet and down the edges of the drop hole can provide a facility that is easier to clean in the short term.

## Slide 34: 6. Sanitation and hygiene facilities -kit
What the Kit contains to achieve safe common sanitation and hygiene areas:
Soap (handwashing and personal hygiene)
10 litre bucket (red), cloths and disinfectant (chlorine)
Scrub brush with handle for latrine cleaning
2 litre plastic container and nylon cord to fabricate tippy tap

## Slide 35: Follow-up actions to sustain cholera transmission interruption in case household
Water: Depending on community chlorination, demonstrate household water chlorination and leave Aquatabs.
Disinfection: Leave household with hygiene kit, and basic handwashing stations, disinfection area and laminated card on disinfection. Introduce hygiene kit and how to disinfect and prevent cross contamination from soiled kit materials.
Food: Give guidance on sufficient cooking (especially seafood), hygiene and protection from insects in food preparation (SHoCH – sterilized, hot, covered, hands*).
Case area: Ensure cases have container for toilet/vomit, easily cleaned, and instruct on emptying safely. Assist in ensuring convalescent area is easily kept clean.
Latrine: Leave materials for disinfecting latrine, handwashing
Case: Ensure cases in house get treatment if cannot hydrate.
*STERILIZED: Seafood boiled 15-20 min. Sterilizing water with chlorine. HOT: Well cooked, served hot. COVERED: Food to be covered to protect from flies; HANDS: practical assistance for hand washing, soap and water or alcohol hand gel
Notes: When they leave they nee dot be sure there are not case that are not treated.

## Slide 36: The Household Hygiene and Disinfection Kit List
Household Kit items (recommended)
10 litre bucket with tap
10 litre bucket
2 litre container (tippy-tap)
Bottle of chlorine
Different colour cloths (clean) Soap: body and laundry
Water treatment products
Nylon cord
Info cards and tape
Scrub brush for toilet cleaning
Items which volunteers should carry to distribute or use where necessary
Chlorine solution
ORS sachets
Water treatment products
Small soap bars
Information cards
Cloth for water filtering
Thick elastic bands
Volunteer use
PPE (Boots, Gloves, googles, apron)
Notes: Slide 30-32 The disinfection kit including practical play with kit.
Check the HH and disinfection material list with the latest kit list.

## Slide 37: Activity 3 (Practical) 3.1 Get familiar with the HH kit 3.2 Get familiar with the volunteer kit 3.3 Scenario Activity
Notes: Have a HH kit and a volunteer kit out for the volunteers to look at.
Introduce the Household Assessment (see separate document: BORT ASS T2 HH) Go through briefly.
Explain that the volunteers will have to make decisions as to whether they leave a kit behind with the household or to just use their own supplies to do a limited number of actions. They will have to make judgements. The scenarios given will get them to think over the issues.
NB. HHs that have had cases recently or currently have suspected cases should always receive a kit.

## Slide 38: 3.1 Get familiar with Household kit
Look at all the items in the Kit one by one
Determine what they are used for and how they are used.
Establish what transmission route each item can interrupt.

## Slide 39: 3.2 Get familiar with the volunteer kit
Look at all the items in the Kit one by one
Determine what they are used for and how they are used.
Establish what transmission route each item can interrupt.

## Slide 40: 3.3 Scenario Activity
Look at the Scenario handout and work through the different scenarios in groups.
This activity will take 40 minutes
Notes: Work in pairs as they would be in the field. Select one scenario for the exercise. Two pax and work with two scenarios (10 mins for one scenario at the same time three groups). 10 mins to present each group (three groups)
Depending on number of participants

## Slide 41: Coordinating Household and Community Interventions
BORT conducts activities in households and shared spaces at the same time
Coordination between the two work parties is important
For example, avoiding the double chlorination of water which may discourage its use.
Information gathered initially from case households can help to make community shared space interventions more effective.
For example, knowing which water sources the case household used, and prioritizing this for treatment.
Notes: Slide 33 The importance of sharing information and actions between those working on shared spaces – understanding risk, reducing duplication and over-chlorination.
1. The main problem with prepositioning in the past has been the storage of chlorine-based products. The branch will have the ability to produce chlorine. If some can be bought quickly locally then it might be used but moving to scale the branch can produce chlorine

## Slide 42: Principles of response
EFFICIENCY
  target where risks are common, acting first to stop the sources that affect the most people
GUIDING and CONTROLLING
  if you rely on complex changing behaviour it will take weeks or months, people will die – give practical support for quick, simple safety improvements.
KEEP IT SIMPLE, MAKE IT CONVENIENT
  Changes you make must be simple (easy to do, not complicated) and convenient (available in the right place) or nobody will apply them

## Slide 43: Key messages
Remove immediate risk:
Chlorinate water in case and nearby homes immediately
Remove risk of material/hand contact with water
Disinfect materials in the case home
Remove contact risk in storage and serving of water
Dispose of food which case has been in contact with
Safe excreta disposal: use of latrines and keep them cleaned
Prevent future risk:
Establish handwashing in homes of case and neighbors
Food hygiene, personal hygiene when in proximity to case and cleaning of sanitation.
Coordinate household information and actions with those aimed at the community
Notes: Summaries
The main problem with prepositioning in the past has been the storage of chlorine-based products. The branch will have the ability to produce chlorine. If some can be bought quickly locally then it might be used but moving to scale the branch can produce chlorine

## Slide 44: Action to prevent COVID-19 transmission
Carry out disinfection of surfaces and shared facilities
Isolate/shield the case ensuring distancing from other households
Ensure rooms are ventilated – air moving through
Encourage regular handwashing in the home and make facilities for this available
Mask wearing (cloth to cover nose and mouth) when in same room as patient
Ensure community support to give supplies, clean water etc for vulnerable people (long term conditions, older) where the household cannot provide this for itself
Notes: Slide 32 – Action to prevent COVID-19. The main point here is that distancing/shielding and ventilation are more effective than disinfection.
* often the floor of latrines will be mud and difficult to clean properly. Situating plastic sheeting around the toilet and down the edges of the drop hole can provide a facility that is easier to clean in the short term.